Instrument layout, gauges and switches

|  | S/C | Roadster | 289 Sport |
| --- | --- | --- | --- |
| Oil Pressure | Smiths full sweep 0-100psi | Smiths full sweep 0-100psi | Smiths full sweep 0-100psi |
| Water Temp | Smiths full sweep 0-110deg C | Smiths full sweep 0-110deg C | Smiths full sweep 0-110deg C |
| Oil Temp | Smiths full sweep 0-140deg C | Smiths full sweep 0-140deg C | Smiths full sweep 0-140deg C |
| Amps | Lucas -50 +50 Needle pointed up | Lucas -50 +50 Needle pointed up | Lucas -50 +50 Needle pointed up |
| Fuel Gauge | None | Smiths half sweep Needle pointed down | Smiths half sweep Needle pointed down |
| Fuel pressure | Smiths full sweep 0-10 psi | None | None |
| Clock | None | None | Smiths Electrical Had two "screws" at 10 and 2 |
| Speedo | Smiths reverse wound 0-180 mph | Smiths reverse wound on early cars Later cars used normally wound 0-180mph | Smiths normally wound 0-180mph |
| Rev (Tacho) | Smiths - same size as speedo 0-8000rpm | Smiths - same size as speedo 0-8000rpm | Smiths - same size as speedo 0-8000rpm |
| Warning lights | Big red for ignition smaller blue and green for bright’s and indicators resp | Big red for ignition smaller blue and green for bright's and indicators resp | Big red for ignition smaller blue and green for bright's and indicators resp |
| Toggle Diff | 2 position (up down) for the diff oil cooler pump | None | None |

| Toggle Fans | 2 position (up down) To override the thermo switch | 2 position (up down) To override the thermo switch | None |
| --- | --- | --- | --- |
| Wiper knob | Fluted knob 3 position (turn) off-slow-fast | Fluted knob 3 position (turn) off-slow-fast | Fluted knob 3 position (turn) off-slow-fast |
| W/screen washer | None | Fluted push pull knob which was actually a pump | ? |
| Toggle fog | 2 position (up down) | ? | None |
| Toggle lights | 3 position (up down) off-parks-lights | 3 position (up down) off-parks-lights | 3 position (up down) off-parks-lights |
| Panel rheostat | Fluted turn knob Could switch panel lights off or just dim them | Fluted turn knob Could switch panel lights off or just dim them | Fluted turn knob Could switch panel lights off or just dim them |
| Hooter | Round black button | Round black button | Round black button |
| Ignition switch | Ignition and starter | Ignition and starter | Ignition and starter |
| Fresh air knob | Fluted push pull knob opened air to footwells | Fluted push pull knob opened air to footwells | Fluted push pull knob opened air to footwells |
| Cigarette lighter | None | Round push-in knob | None |